## Slide 1: – CWZ Standard – Diagrams
Manny Insignares
March 21 2024

## Slide 2: CWZ Reference Architecture

## Slide 3
Connected Work Zone Physical Architecture
Work Zone Center
Traffic Management Center
External
Consumer Center
WorkZoneFeed
Traffic Management Center
DeviceFeed
Work Zone Center
External
Consumer Center
DeviceFeed
Work Zone Data Exchange
External Consumer
Center
Traffic Management Center
WZ Data Exchange Intermediary
WorkZoneFeed
WorkZoneFeed
Work Zone Data Exchange with Intermediary
Traffic Management
Center
Work Zone Center
WZ Data Exchange Intermediary
DeviceFeed
DeviceFeed
External Consumer
Center
Work Zone Center
WZ Data Exchange Intermediary
DeviceFeed
DeviceFeed

## Slide 4
Connected Work Zone Physical Architecture
(Compatibility with the Connected Vehicle Environment)
Generic Vehicle
(OBU)
Traffic Management Center
Roadside
Unit
(RSU)
NTCIP 1218
J2945/4 RSM
Compatibility with the Connected Vehicle Environment
This diagram will be included in an Annex that will contain guidance for connected work zones that will deploy elements of the connected vehicle environment.

## Slide 5: ARC-IT Service Package Diagram
Data Structure

## Slide 6
MC06: Work Zone Management

## Slide 7: CWZ Standard ConOps
Data Structure

## Slide 8
CWZ ConOps – Work Zone Information Organization
Zone Metadata
Zone Status
Zone Lanes
Zone Speed Limit
Zone Device
Zone Traffic Data
Zone Information
Zone Location
Zone Schedule
Zone Work Vehicle Device
Zone VRU Device

## Slide 9: WZDX Work Zone Feed
Data Structure

## Slide 10
road event feed info
data source
event type
related road events
road names
direction
name
description
creation date
update date
relationship
WZDX 4.1 – Work Zone Feed Data Structure
feed info
Feature Collection
feature
properties
core details
location description
verification status
dates
vehicle travel impact
location method
worked presence status
speed limits
restriction geometry descriptions
types of work
lanes status and description
geometry
LineString
MultiPoint
bbox
bbox
Work Zone Feed

## Slide 11: WZDX Work Zone Device Feed
Data Structure

## Slide 12
Work Zone Device Feed
WZDX 4.1 – Device Feed Data Structure (1/3)
feed info
Feature Collection
feature
properties
(varies with device)
core details (FieldDevice)
(device specific properties)
geometry
bbox
bbox
device type
data source
device status
update date
has automatic location
road direction
road names
name (of device)
description
status messages
is moving
road event ids
milepost
make
model
serial number
firmware version
id

## Slide 13
WZDX 4.1 – Device Feed Data Structure (2/3: Arrow Board, Camera, Dynamic Message Sign, Flashing Beacon)
feed info
Feature Collection
feature
properties
(varies with device)
core details (FieldDevice)
Arrow Board
Camera
Dynamic Message Sign
geometry
bbox
bbox
pattern
is_in_transport_position
image_url
image_timestamp
message_multi-string
Flashing Beacon
function
is_flashing
sign_text
id
Arrow Board
Camera
Dynamic Message Sign
Arrow Board
Camera
Work Zone Device Feed

## Slide 14
Work Zone Device Feed
WZDX 4.1 – Device Feed Data Structure (3/3: Hybrid Sign, Location Marker, Traffic Sensor)
feed info
Feature Collection
feature
properties
(varies with device)
core details (FieldDevice)
Hybrid Sign
Location Marker
Traffic Sensor
geometry
bbox
bbox
marked_locations * (array)
road_event_id
collection_interval_start_date
collection_interval_end_date
average_speed_kph
volume_vph
occupancy_percent
lane_data
afad
delineator
flagger
lane-shift
lane-closure
personal-device
temporary-traffic-signal
ramp-closure
road-closure
road-event-start
road-event-end
work-zone-start
work-zone-end
marked_locations type *
Traffic Sensor Lane Data
lane_order
road_event_id
average_speed_kph
volume_vph
occupancy_percent
dynamic_message_function
dynamic_message_text
static_sign_text
id
Hybrid Sign
Location Marker

## Slide 15: J2945/4
Data Structure

## Slide 16
J2945/4 Road Safety Message Data Structure (1/4: Common Container -> Event Info)
Road Safety Message
commonContainer
eventInfo
eventID
eventUpdateCount “revision number”
startDateTime
endDateTime
causeCode & subCauseCode
regionInfo
affectedVehicles
endDateTime
eventReccurence
eventCancellation
contentContainer
situational container
incident container
reduced speed zone container
lane closure container

## Slide 17
J2945/4 Road Safety Message Data Structure (2/4: Content Container -> Region Info)
Road Safety Message
commonContainer
eventInfo
approachRegion
applicableHeading
locationUncertainty
endDateTime
regionInfo
referencePointType
descriptiveName
referencePoint
contentContainer
situational container
incident container
reduced speed zone container
lane closure container

## Slide 18
J2945/4 Road Safety Message Data Structure (3/4: Content Container -> Reduced Speed Zone Container & Lane Closure Container)
Road Safety Message
common Container
reduced Speed Zone Container
content Container
(one of)
regulatory speed limit
Region Info
(see 2/4)
lane Closure Container
lane status
Region Info
(see 2/4)
lane position
lane close offset
lane closed
lane status varies
situational container
incident container

## Slide 19
J2945/4 Road Safety Message Data Structure (4/4: Content Container -> Situational Container & Content Container -> Incident Container)
Road Safety Message
common container
reduced speed zone container
incident container
content container
(one of)
lane closure container
situational container
obstructions
applicable region
(see Region Info 2/4)
location
description
anomalous traffic
people present
responder type
incident location
(see Region Info 2/4)